Copyright 2018 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek, Inc. for the AIA

This Product MasterSpec Section is licensed by Deltek, Inc. to Potter Roemer Fire Pro, Morris Group International ("Licensee").

This Product MasterSpec Section modifies the original MasterSpec text and does not include the full content of the original MasterSpec Section.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, Deltek or The American Institute of Architects (AIA). Neither AIA nor Deltek are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact Potter Roemer Fire Pro, Morris Group International, 17451 Hurley Street, City of Industry, CA 91744; Phone: (800) 366-3473 | (626) 855-4890; Fax: (888) 404-7960; Website: https://www.potterroemer.com/home; Email: info@potterroemer.com.

For information about MasterSpec, contact Deltek at (800) 424-5080 or visit masterspec.com.

SECTION 104416 - FIRE EXTINGUISHERS

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Access Product MasterSpec Sections:

<Double click here to view the list of manufacturer Sections available at ProductMasterSpec.com.>

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Retain or delete this article in all Sections of Project Manual.

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

SUMMARY

Section includes portable, hand-carried fire extinguishers[ and mounting brackets for fire extinguishers].

Related Requirements:

Retain subparagraphs below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 104413 "Fire Protection Cabinets."

Section 211100 "Facility Fire-Suppression Water-Service Piping" for hose systems, racks, and valves.

Section 233813 "Commercial-Kitchen Hoods" for fire-extinguishing systems provided as part of commercial-kitchen exhaust hoods.

ACTION SUBMITTALS

Product Data: For each type of product. Include rating and classification, material descriptions, dimensions of individual components and profiles, and finishes for fire extinguisher[ and mounting brackets].

Product Schedule: For fire extinguishers. Coordinate final fire-extinguisher schedule with fire-protection cabinet schedule to ensure proper fit and function.[ Use same designations indicated on Drawings.]

INFORMATIONAL SUBMITTALS

Warranty: Sample of special warranty.

CLOSEOUT SUBMITTALS

Operation and Maintenance Data: For fire extinguishers to include in maintenance manuals.

COORDINATION

Consider retaining this article if fire-protection cabinets are specified by series only or for complex projects.

Coordinate type and capacity of fire extinguishers with fire-protection cabinets to ensure fit and function.

WARRANTY

When warranties are required, verify with Owner's counsel that special warranties stated in this article are not less than remedies available to Owner under prevailing local laws.

Special Warranty: Manufacturer's standard form in which manufacturer agrees to repair or replace fire extinguishers that fail in materials or workmanship within specified warranty period.

Failures include, but are not limited to, the following:

Hydrostatic test in first subparagraph below is required every five years for water, AFFF, dry-chemical-in-stainless steel-shell, carbon dioxide, and wet-chemical fire extinguishers; test is required every 12 years for other dry-chemical, dry-powder, and halogenated-agent fire extinguishers.

Failure of hydrostatic test in accordance with NFPA 10 when testing interval required by NFPA 10 is within the warranty period.

Faulty operation of valves or release levers.

Verify available warranties and warranty periods for fire extinguishers with manufacturers.

Warranty Period: [Six] <Insert number> years from date of Substantial Completion.

PRODUCTS

Manufacturers and products listed in SpecAgent and MasterWorks Paragraph Builder are neither recommended nor endorsed by the AIA or Deltek. Before inserting names, verify that manufacturers and products listed there comply with requirements retained or revised in descriptions and are both available and suitable for the intended applications. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

PERFORMANCE REQUIREMENTS

NFPA Compliance: Fabricate and label fire extinguishers to comply with NFPA 10, "Portable Fire Extinguishers."

Fire Extinguishers: Listed and labeled for type, rating, and classification by an independent testing agency acceptable to authorities having jurisdiction.

Retain subparagraph below if required for insurance purposes; verify availability with manufacturers because not all products comply.

Provide fire extinguishers approved, listed, and labeled by [UL] [and] [FM Global].

PORTABLE, HAND-CARRIED FIRE EXTINGUISHERS

Fire Extinguishers: Type, size, and capacity for each [fire-protection cabinet] [and] [mounting bracket] indicated.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Potter Roemer Fire Pro, Morris Group International; Models as specified below or comparable product by one of the following:

Amerex Corporation.

Ansul by Johnson Controls Company.

Babcock-Davis.

Badger Fire Protection.

Buckeye Fire Equipment Company.

Fire End & Croker Corporation.

JL Industries, Inc.; a division of the Activar Construction Products Group.

Kidde Residential and Commercial Division.

Larsens Manufacturing Company.

Nystrom.

<Insert manufacturer's name>.

Retain "Source Limitations" Paragraph below if requiring fire extinguishers and fire-protection cabinets to be from same manufacturer. Verify availability with manufacturers.

Source Limitations: Obtain fire extinguishers, fire-protection cabinets, and accessories, from single source from single manufacturer.

Valves: Manufacturer's standard.

Handles and Levers: Manufacturer's standard.

Instruction Labels: Include pictorial marking system complying with NFPA 10, Appendix B[, and bar coding for documenting fire-extinguisher location, inspections, maintenance, and recharging].

In remaining paragraphs, the letter A, B, C, D, or K indicates the class of fire on which an extinguisher is effective. Class A and Class B are preceded by a rating numeral indicating the extinguisher's relative extinguishing effectiveness. Extinguishers for Class C, Class D, and Class K fires are not required to have a rating numeral. See the Evaluations for fire classifications and numerical rating explanation.

In retained paragraphs below, insert drawing designation. Use these designations on Drawings to identify each product.

Multipurpose Dry-Chemical Type in Steel Container <Insert drawing designation>: UL-rated [1-A:10-B:C, 2.5-lb (1.1-kg)] [2-A:10-B:C, 5-lb (2.3-kg)] [3-A:40-B:C, 5-lb (2.3-kg)] [3-A:40-B:C, 6-lb (2.7-kg)] [4-A:80-B:C, 10-lb (4.5-kg)] [20-A:120-B:C, 20-lb (9.1-kg)] nominal capacity, with monoammonium phosphate-based dry chemical in enameled-steel container.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3002] [3005] [3005-5] [3006] [3010] [3020] or comparable product.

Carbon Dioxide Type <Insert drawing designation>: UL-rated [5-B:C, 5-lb (2.3-kg)] [10-B:C, 10-lb (4.5-kg)] [10-B:C, 15-lb (6.8-kg)] [10-B:C, 20-lb (9.1-kg)] nominal capacity, with carbon dioxide in enameled-aluminum container.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3405] [3410] [3415] [3420] or comparable product.

"Halotron 1 Clean-Agent Type in Steel Container" Paragraph below describes Potter Roemer's fire extinguishers using clean agent as an alternative to halon. See the Evaluations.

"Halotron 1" Clean-Agent Type in Steel Container <Insert drawing designation>: UL-rated [1B:C, 1.4-lb (.63-kg)] [2B:C, 2.5-lb (1.1-kg)] [5-B:C, 5-lb (2.2-kg)] [1-A:10-B:C, 11-lb (5-kg)] [2-A:10-B:C, 15.5-lb (7-kg)] nominal capacity, with HFC blend agent and inert material in enameled-steel container; with pressure-indicating gauge.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3101] [3102] [3105] [3111] [3115] or comparable product.

Retain one or more of first two paragraphs below for stored-pressure water-type extinguishers. Potential for freezing exists with all types.

Stored-Pressure Water Type <Insert drawing designation>: UL-rated 2-A, 2.5-gal. (9.5-L) nominal capacity, with water in stainless steel container; with pressure-indicating gauge.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model 3202 or comparable product.

Stored-Pressure Water-Mist Type <Insert drawing designation>: UL-rated 2-A:C, 2.5-gal. (9.5-L) nominal capacity, with water in enameled-steel container; with pressure-indicating gauge.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model 3272 or comparable product.

Pressurized, AR-AFFF-Foam Type <Insert drawing designation>: UL-rated 3-A:20-B, 2.5-gal. (9.5-L) nominal capacity, with AR-AFFF foam in stainless steel container; with pressure-indicating gauge.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model 3250 or comparable product.

"K Class" Wet-Chemical Type <Insert drawing designation>: UL-rated 2-A:K, [1.6-gal. (6-L)] [2.5-gal. (9.5-L)] nominal capacity, with potassium acetate-based chemical in stainless steel container; with pressure-indicating gauge.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3260] [3262] or comparable product.

Retain first paragraph below for regular dry-chemical-type extinguishers.

Regular Dry-Chemical Type in Steel Container <Insert drawing designation>: UL-rated [10-B:C, 2.5-lb (1.1-kg)] [10-B:C, 5-lb (2.3-kg)] [40-B:C, 5.5-lb (2.5-kg)] [40-B:C, 6-lb (2.7-kg)] [60-B:C, 10-lb (4.5-kg)] [120-B:C, 20-lb (9.1-kg)] nominal capacity, with sodium bicarbonate-based dry chemical in enameled-steel container.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3302] [3305] [3305-5] [3306] [3310] [3320] or comparable product.

Retain first paragraph below for multipurpose dry-chemical-type extinguishers.

Multipurpose Cartridge-Operated Dry-Chemical Type in Steel Container <Insert drawing designation>: UL-rated [4-A:60B:C, 10-lb (4.5-kg)] [20-A:80B:C, 20-lb (9-kg)] [20-A:120B:C, 25-lb (11.3-kg)].

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model [3052] [3054] [3056] or comparable product.

Retain paragraph below for Purple-K cartridge-operated dry-chemical-type extinguishers.

Purple-K Cartridge-Operated Dry-Chemical Type in Steel Container <Insert drawing designation>: UL-rated 120-B:C, 28.5-lb (13-kg) nominal capacity, with potassium bicarbonate-based dry chemical in enameled-steel container.

Retain "Basis-of-Design Product" Subparagraph below to require a specific product or a comparable product.

Basis of Design: Potter Roemer Fire Pro, Morris Group International; Model 3356 or comparable product.

Insert other types and capacities to suit Project.

MOUNTING BRACKETS <Insert drawing designation>

Retain this article if mounting brackets separate from fire-protection cabinets are required.

Copy this article and re-edit for each product.

Insert drawing designation. Use these designations on Drawings to identify each product.

Mounting Brackets: Manufacturer's standard steel, designed to secure fire extinguisher to wall or structure, of sizes required for types and capacities of fire extinguishers indicated, with red baked-enamel finish.

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

          - Basis-of-Design Product: Subject to compliance with requirements, provide Potter Roemer Fire Pro, Morris Group International; Model 3900 Series or comparable product by one of the following:

Amerex Corporation.

Ansul by Johnson Controls Company.

Babcock-Davis.

Badger Fire Protection.

Buckeye Fire Equipment Company.

Fire End & Croker Corporation.

JL Industries, Inc.; a division of the Activar Construction Products Group.

Kidde Residential and Commercial Division.

Larsens Manufacturing Company.

Nystrom.

<Insert manufacturer's name>.

Retain "Source Limitations" Paragraph below if requiring mounting brackets and fire extinguishers to be from same manufacturer. Verify availability with manufacturers.

Source Limitations: Obtain mounting brackets and fire extinguishers from single source from single manufacturer.

Identification: Lettering complying with authorities having jurisdiction for letter style, size, spacing, and location. Locate as indicated by Architect.

Identify bracket-mounted fire extinguishers with the words "FIRE EXTINGUISHER" in red letter decals applied to mounting surface.

If more than one orientation is required, indicate location of each on Drawings.

Orientation: [Vertical] [Horizontal].

EXECUTION

EXAMINATION

Examine fire extinguishers for proper charging and tagging.

Remove and replace damaged, defective, or undercharged fire extinguishers.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

General: Install fire extinguishers[ and mounting brackets] in locations indicated and in compliance with requirements of authorities having jurisdiction.

Retain "Mounting Brackets" Subparagraph below if retaining option in "General" Paragraph above. If more than one height is required, indicate locations for each height. According to NFPA 10, maximum mounting height for fire extinguishers weighing 40 lb (18 kg) or less is 60 inches (1524 mm) from finished floor to top of extinguisher; for those weighing more, it is 42 inches (1067 mm) from finished floor to top of extinguisher. In rooms required to comply with ADA-ABA Guidelines, mounting height for fire extinguishers is not to exceed 48 inches (1219 mm) to the handle.

Mounting Brackets: Top of fire extinguisher to be at [42 inches (1067 mm)] <Insert dimension> above finished floor.

Mounting Brackets: Fasten mounting brackets to surfaces, square and plumb, at locations indicated.

END OF SECTION 104416